## Slide 1: How do you get data into (and out of) a computer?
Part 1: Introduction to Data Acquisition (DAQ) - Input

## Slide 2: Data Acquisition (DAQ)
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
Without DAQ, then we would all be theoretical neuroscientists.
Lisbon
> 33
What is the
temperature
outside?
How do you get
that value into
a computer?

## Slide 3: Data Acquisition (DAQ)
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
Anything is measurable…and everyone should no how to do this.
Binary Data
“Real Value”
Transfer
ADC
RAM
(“Variable”)
Display
Storage
MonitorHDD
(“File”)
00100001
Protocol
Computer
System
Memory
Protocol
Voltage
+2.43 V
33° C
Sensor
V= IR
Digitization
> 33
Lisbon

## Slide 4: Sensor (voltage transducer)
Computers can only measure voltage. Therefore, any real-world quantity must be converted into a voltage before it can be measured and digitized.
“Real Value”
Voltage
+2.43 V
33° C
V= IR
Sensor
LDR, Thermistor, Photodiode, etc.
Camera, E-phys System
Microphone, Keyboard, Touchscreen

## Slide 5: Ohm’s Law
A linear relationship between Voltage, Current and Resistance exists for “Ohmic” circuit elements. This
This linear relationship between passive circuit elements will solve the majority of electronics dilemmas.
“Real Value”
Voltage
+2.43 V
33° C
V= IR
Sensor
V = IR
Ohm’s Law
Ohm
V - Voltage: Force pushing electrons
(Volts)
I - Current: Number of electrons/second
(Amps)
R - Resistance: Ease to electron flow
(Ohms)

## Slide 6: Voltage Divider
Two resistors will proportionally attenuate a voltage as current flows from a source to ground. This relationship can be used to create an intermediate voltage dependent on a variable resistor.
This circuit is everywhere in modern circuits. A sensor can be constructed by simply making one of the resistors dependent on a “real world” quantity. (pressure, temperature, light, rotation…sweat…anything!)
“Real Value”
Voltage
+2.43 V
33° C
V= IR
Sensor
Voltage Divider

## Slide 7: Analog to Digital Converter (ADC)
An integrated circuit that converts analog values to binary (digital) representation. They come in many flavours, speeds and bit depths.
ADCs are everywhere. In your digital cameras, smartphone, and GPS. Everything a computer knows about the “real-world” goes through an ADC. There are many types, with many different features (speeds, resolution, noise, channels…).
Binary Data
ADC
00100001
Voltage
+2.43 V
Digitization
An ADC converts analog voltage to a binary representation.
(Relevant Characteristics)
- How fast? (Sample Rate, Hz)
- Resolution? (#bits per sample)
- Range (of input voltage)

## Slide 8: Digital Input
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
The “simplest” computer input. 0 or 1.
Binary Data
ADC
0 or 1
Voltage
0 to 5 V
Digitization
Voltage Comparator
The simplest ADC: 1-bit

## Slide 9: Analog Input: Flash ADC
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
An easy to understand, but not often used version of an ADC. Very, very fast…but low bit depth.
Binary Data
ADC
00100001
Voltage
0/+5 V
Digitization
Serial Voltage Divider
Comparator
Flash ADC
Fast
Low Bit Depth
Large!

## Slide 10: Analog Input: Successive Approximation ADC
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
Much more common form of ADC.
Binary Data
ADC
00100001
Voltage
0/+5 V
Digitization
Successive Approximation ADC
Slow(er)
High Bit Depth
Small

## Slide 11: Communication Protocol
A standard procedure for transferring binary information between digital devices,
Binary Data
Transfer
RAM
(“Variable”)
00100001
Protocol
Computer
System
Memory

## Slide 12: Serial Port (USART/USART – RS-232)
A standard procedure for transferring binary information between digital devices,
Binary Data
Transfer
RAM
(“Variable”)
00100001
Protocol
Computer
System
Memory

## Slide 13: System Memory (RAM)
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
You can only “work” with data in System memory. This is where you can start doing analysis…roting data to other devices for control of storage. This is when your data is IN the computer.
Binary Data
Transfer
RAM
(“Variable”)
00100001
Protocol
Computer
System
Memory

## Slide 14: Data Display/Storage
This is technically data “output”…but just for completeness.
RAM
(“Variable”)
Display
Storage
MonitorHDD
(“File”)
Computer
System
Memory
Protocol

## Slide 15: Data Acquisition (DAQ)
The process of measuring a real-word value via voltage conversion, digitization, and transfer to system memory. (for subsequent processing and storage).
This is how computers know about the world.
Binary Data
“Real Value”
Transfer
ADC
RAM
(“Variable”)
Display
Storage
MonitorHDD
(“File”)
00100001
Protocol
Computer
System
Memory
Protocol
Voltage
+2.43 V
33° C
V= IR
Digitization
Sensor

## Slide 16: Microcontroller Worksheet
DAQ and Control with a simple microcontroller.
We

## Slide 17: How do you get data into (and out of) a computer?
Part 2: Introduction to Actuation– Output

## Slide 18: Control (with a binary computer)
Conversely to acquisition, computers can only output voltages.
If you want to…
“Play a tone”
“Make something move”
“Turn on a light”
“Open a valve”
“Show a movie”
… etc.
RAM
(“Variable”)
Computer
System
Memory
Protocol
“The External World”

## Slide 19: Control (with a binary computer)
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Computer
System
Memory
Digital Output
LED
DC Motor
Sound
Card
Solenoid
Relay
Monitor
“Hobby”
Servo
HDD
Laser Diode
Galvo Mirror
Computer Peripherals
TTL
Specialized
VGA, HDMI
SATA
MIDI
Analog Output
PWM / FM
Protocol
DAC
Pseudo-Analog Output
Piezo
Buzzer

## Slide 20: Digital Output
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Computer
System
Memory
Digital Output
LED
DC Motor
Solenoid
Relay
TTL
Protocol
ON vs OFF

## Slide 21: TTL: Transistor-Transistor Logic
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Computer
System
Memory
Digital Output
LED
TTL
Protocol
0 to +5 Volts

## Slide 22: Digital Output
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Computer
System
Memory
Digital Output
LED
DC Motor
Solenoid
Relay
TTL
Protocol
~10 mA
Can you start (“jump”) your car with a USB port?

## Slide 23: Electrical Load
An element in a circuit that consumes power. The more power consumed, the “heavier” the load.
RAM
(“Variable”)
Computer
System
Memory
Digital Output
Electric Car
Engine?
TTL
Protocol
Power = V*I = V*R2

## Slide 24: Digital Output (Heavy Loads: > 100 mA)
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Display
Storage
Motor
Computer
System
Memory
Protocol
- “Make something move”
- “Turn on the room lights”
“Drive a high power laser”
…

## Slide 25: Transistor (MOSFET) Switch
PN-Junction, Gate, Holes, Doping, and more!

## Slide 26: The Silicon Transistor
PN-Junction, Gate, Holes, Doping, and more!

## Slide 27: Transistor: Switching Inductive Loads
Current caused by induction can cause negative current flow (backwards), which can damage
Protection Diode

## Slide 28: Analog Output
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Display
Storage
0101001
Computer
System
Memory
Protocol
Display
Storage
+3.72 V
DAC

## Slide 29: Digital-to-Analog Converter (DAC)
Conversely to acquisition, computers can only output voltages.
RAM
(“Variable”)
Display
Storage
0101001
Computer
System
Memory
Protocol
Display
Storage
+2.31 V
DAC
Note: The Arduino Uno has no DACs.

## Slide 30: Pulse-Width Modulation (PWM)
Pesudo-Analog Output. Duty-cycle approximates an analog value.
RAM
(“Variable”)
Display
Storage
“Hobby Servo”
Computer
System
Memory
Protocol
PWM
(approx. sinewave)

## Slide 31: Vehicle Project
Autonomous Braitenberg vehicles that follow (or avoid) light.